## Slide 1: US Powerboating Safe Powerboat Handling / Safety and Rescue Boat Handling Day Two

## Slide 2: Navigation Rules
Rules of the Road SPR p.107
  Inland Rules vs International
  Maintain proper lookout
  Safe speed
  Operating in narrow channels
    Vessels less than 20m SHALL NOT impede passage of a vessel that can only operate in the channel
    A vessel engaged in fishing (NOT trolling) shall not impede the passage of any other vessel
    On rivers (Inland Rules): vessels proceeding downbound (w/the current) shall have right-of-way over an upbound vessel
  Sounds signals
    Can provide information such as which side you are passing on, to indicate danger or confusion or as an alert in fog

## Slide 3: Navigation Rules
Rules of the Road
  Rule 2 of the Navigation Rules
    “Nothing in these Rules shall exonerate any vessel, or the owner, master or crew thereof, from the consequences of any neglect to comply with these rules…or by the special circumstances of the case.”
  Rule 7 of the Navigation Rules
    “Every vessel shall use all available means appropriate to the prevailing circumstances and conditions to determine if risk of collision exists. If there is any doubt such risk shall be deemed to exist.

## Slide 4: Navigation Rules
Rules of the Road SPR p.109, 110
  Head on
  Starboard over Port
  Overtaken over Overtaking (Clear ahead over clear astern)
  Sail over Power (unless in a channel)

## Slide 5: Navigation Rules
Rules of the Road
  Vessels underway must always keep clear of:
      A vessel not under command (ie. Adrift or on fire)
      A vessel that is restricted in its ability to maneuver (ie. Dredging)
      A vessel engaged in fishing with nets, lines or trawls
          DOES NOT include fishing with trolling lines
  Remember – the stand on vessel has the right way, the give way vessel must alter her course
  A formal accident report must be submitted within 48 hours if a person dies, there are injuries requiring more than first aid or if there is more than $2000 in damage. SPR p.90

## Slide 6: Navigation Rules
Rules of the Road – Right Away Rules
Only Overtaken
New Not under command
Reels Restricted in its ability to maneuver
Catch Constrained by draft
Fish Fishing
So Sailing
Purchase Power driven vessel
Some Seaplane
Worms WIG

## Slide 7: Navigation Rules
Rules of the Road
  Light schemes
    Masthead light = white light 225 fixed to show light from right ahead to 22.5 abaft the beam on either side
    Sidelights = 112.5 green light on the starboard side and a 112.5 red light on the port side fixed to show light from right ahead to 22.5 abaft the beam
    Sternlight = 135 white light placed near or at the stern fixed to show the light 67.5 from right aft on each side of the vessel
    All-round light = 360 light

## Slide 8: Navigation Rules
Rules of the Road
  Light schemes
    Power driven vessels less than 12 meters in length must exhibit a masthead light, sidelights and sternlight while underway
      An all-round white light may be substituted for the masthead light and sternlight
    Vessels under sail must exhibit sidelights and a sternlight
    Vessels less than 50 meters at anchor must exhibit an all-round white light where it can best be seen

## Slide 9: Navigation Rules
Rules of the Road SPR p.108
  How to determine if risk of collision exists (handout):
    Constant Bearing Decreasing Distance
    When In Doubt, risk is assumed to exist!

## Slide 10: Navigation Rules
Rules of the Road
  What is bearing drift? (handout)
      Bearing taken relative to you or your boat

## Slide 11: Navigation Aids
Aids to Navigation SPR p.120 and CD
  Lateral Marks – system of lateral marks used to indicate on which side a mark should be passed when returning from seaward
    In US waters, red marks are kept on the starboard side; green marks are kept on the port side
    When an approach from seaward cannot be determined, the Conventional Direction is used, which is a clockwise rotation around the US.
      On Lake Michigan, a southerly direction is considered returning from sea
  RED AND GREEN MARKS
    PORT LATERAL MARKS will be green, odd numbered cans or squares
    STARBOARD LATERAL MARKS will be red, even numbered nuns or triangles
    PREFERRED CHANNEL MARKS will be red and green banded and can be any of the above shapes (nuns, cans, squares or triangles)
    ALL MARKS can be daymarks, bouys, lit or unlit, flashing or solid, with sound or without
  Other marks include safe water marks, isolated danger marks, special purpose marks and information/regulatory marks
  Your chart will indicate the type of mark you are expecting

## Slide 12: Navigation Aids
Aids to Navigation SPR p.120 and CD
  Some tricks:
    Red – Right – Returning // Green – Going – Out
      Retuning from sea – clockwise direction around the US
      Entering a harbor is always ‘returning from sea’
    7-UP = green can with odd number
    On the ICW, yellow triangles indicate shoreward side of channel and squares indicate the seaward side. Think triangles for mountains

## Slide 13: Navigation and Piloting SPR p.112
Parallels of Latitude (0-90 north and 0-90 south of Equator)
Meridians of Longitude (0-180 west and 0-180 east of Greenwich)
  Latitude and Longitude
    Measured in degrees, minutes and seconds
    Many charts use decimals of degrees and minutes (they do not include seconds)
    60 sec = 1 min = 1 nautical mile
    60 min = 1 degree
    Every 15 degrees = one time zone (360 / 24hrs = 15)
  ALWAYS measure distance on the LAT scale
  Preciseness is key

## Slide 14: Navigation
Compass SPR p.118
  Variation – difference in degrees between your compass readings and true north
      Changes with location
  Deviation - difference in compass readings created y their magnetic influence
  Compass Error = sum of variation and deviation expressed in degrees E or W
      ex. If, for your onboard compass and location, variation = 9W and deviation = 4E then CE = 5W
      SO, if the true course on the map was 054, you would steer 059 with your onboard compass
      GPS is always TRUE!

## Slide 15: Navigation
Charting tools:
  Parallel rules
  Dividers
  Drawing compass
  Drawing triangles

## Slide 16: Navigation
Ranges SPR p.132
Tides SPR p.105 and SRS Supplement

## Slide 17: Capsize Recovery Methods
Page 17-35 SRS
2 types of capsized vessels
  Surface capsize and turtle
Approach vessel slowly from downwind towards the mast.
  Make sure you can see all sailors before you get too close.
  Assist as requested.
Potential challenges
  Mast stuck in mud, wrapped lines, cleated sails, sailor caught in lines or underneath boat, etc.
Let’s review the section in the book…

## Slide 18: Capsize Recovery Methods

## Slide 19: Towing
Page 47-52 SRS and p.142 SPR
Five Types of towing methods
  Single-line
  Pram variation
  Double-line
  Herringbone Tow
  Towing alongside
COMMUNICATION IS KEY!

## Slide 20: Towing
Use proper driving technique while towing
  Accelerate and decelerate at a constant rate to avoid jerking or severe line slack.
  Make sure to inform the towed vessel driver to steer at your transom (avoid the waterskier effect).
  Mainsails should be lowered BEFORE you pick up the sailboat.
    In any kind of breeze it is dangerous to tow a boat with the mainsail up in any direction but directly upwind.
  If you are towing multiple boats and one falls off the tow, maintain tension for the remaining boats and circle around to pick them up.

## Slide 21: Towing - CYC
Prep the boat before you get there.
  Radio boat to be assisted and make sure they have a proper towing line.
    Line should be tied around the mast of the sailboat. (or the bow cleat**)
  Attach bridle.
  Approach sailboat from downwind
  Keep an appropriate distance – factor in wind and waves.

## Slide 22: Towing
Alongside tow

## Slide 23
BREAK

## Slide 24: Anchoring SPR p.71
Types of anchors
  Danforth-type
  Bruce
  Plow
  Mushroom
Rode = anchor line
Scope = length of rode / (water depth + freeboard)
  5:1 for lunch; 7:1 or more for extended stays or strong winds/seas
Setting and retrieving an anchor – let’s look at pages 73-75

## Slide 25: Emergency Procedures
Conducting a Search (SRS Supp. p. 8-12)
  Item in sight
      Mark position w/ GPS or Loran and throw visible flotation
      Proceed with PIW recovery
  Item is not in sight but incident was recent
      Mark position w/ GPS or Loran
      Commence modified Williamson Turn
      Assign visual search sectors to passengers
          Scan using regularly spaced eye movements
      If loss involves human life, place a Mayday or Pan-Pan
      If no luck, return to estimated position of loss and set up a search pattern

## Slide 26: Emergency Procedures
Conducting a Search (SRS Supp. p. 8-12)
  Item is not in sight and incident is not recent
      Set up a search pattern
          Datum = anchor of pattern
          Types of search patterns:
            Expanding square search
            Parallel track search
            Along track ladder search
            Sector search (multiple and single units)

## Slide 27: VHF Protocol and Usage
Page 4 SRS
Channels:
  16 – Emergencies, hailing
  09 – Recreational hailing
  22 – Coast Guard
  VHF channels are monitored by the USCG, Chicago Marine Police and others
  It is against the law to use these channels improperly
      They can find you!

## Slide 28: VHF Protocol and Usage
Securite
Pan-Pan
Mayday

## Slide 29: VHF Protocol and Usage
How to operate (demo)
Things to remember
    Position VHF perpendicular to the wind or directly downwind
    The Hi/Lo function ONLY affects your transmitting power – it does not increase your receiving power
    The antenna is most effective held straight up and down as high as you can hold it
    Wait a second after depressing the call button before speaking (it will save people a lot of frustration)
    BE SUCCINCT! It is not a telephone. Have a point and get to it quickly.

## Slide 30: VHF Protocol and Usage
Proper radio protocol
  16/9 Channel
  Channels
    Tag
  Squelch
  Volume
  Scan
    Dual
  H/L
    Lock
  CH/WX
    U/I/C

## Slide 31: Boat Operation
Steering a range (inbound and outbound)
Position relative to moving vessel
Boat handling in adverse weather conditions
Capsize boat recovery

## Slide 32: Knots
Quick release
Bowline on a bight
Bowline w/half-hitch
Rolling hitch
Towing bridle

## Slide 33
REVIEW QUESTIONS

## Slide 34
LUNCH