## Slide 1: Safe Powerboat Handling
US Powerboating
Classroom Session One
Powerpoint 1 of 2

## Slide 2: Hull Types & Characteristics
Flat Hulls [SPR p.4]
  Easily get on a plane at high speeds
  Designed for calm, flat water
  Not very stable
  Excessive slide when maneuvering

## Slide 3: Hull Types & Characteristics
Deep V [SPR p.5]
  Similar to flat bottom, but designed to cut through water
  Good steering ability at high speeds
  Perform well in waves in speed; tend to roll at rest

## Slide 4: Hull Types & Characteristics
Cathedral Hull [SPR p.5]
  Two or three v-shapes forward, flat in back
  Good stability at rest and speed
  Rough in speed in waves
  Usually have lower freeboard

## Slide 5: Hull Types & Characteristics
Soft-Inflatable Hull [SPR p.5]
  Poor driving ability (excessive slide)
  High stability
  High load capacity
  Very wet ride

## Slide 6: Hull Types & Characteristics
Rigid-Inflatable Hull [SPR p.4]
  Rigid v-bottom
  High stability
  High load capacity
  Exceptional seaworthiness in rough weather

## Slide 7: Hull Types & Characteristics
Multi-Hulls [SPR p.6]
  Resist rolling
  Good steering ability at speed
  Large turning radius
  Shallow draft

## Slide 8: Hull Types & Characteristics
Round Bottom [SPR p.4]
  Displacement hull
  Glide through water efficiently
  Usually have keel or chine for stability
  Good load bearing capability

## Slide 9: Parts of the Boat
SPR p.11

## Slide 10: Propellers
SPR p.8
How propellers work
  Thrust
  Rotation [right-screw most popular]
    Side force (prop walk)
      More noticeable in reverse – esp. on fixed propeller
  Diameter
  Pitch
    Distance propeller would move in one revolution if turning in solid material
      ie 17” pitch propeller would move 17” inches
  Propeller size = diameter + pitch
    Smaller diameter + higher pitch used on high-speed boats
    Larger diameter + lower pitch used on slow-speed boats
  Stainless steel vs. Aluminum
  Linkage p.16

## Slide 11: Maneuvering Concepts
SPR p.44
Uncontrollable forces affecting a boat
  Wind p.44
    Windage causes bow to fall off and boat to drift sideways
    Increased freeboard = increase windage effect
    Windage affects your turning arc
  Current
    Will move boat along as if on a conveyor belt
    Size, shape, etc. do not matter – current effects all things equally

## Slide 12: Maneuvering Concepts
SPR p.41, 44
How Boats Turn
  Directed Thrust p.41
    Outboards, stern drives and jet drives
    When a propeller is turned at an angle, its thrust is directed at an angle, which turns the boat
    If propeller is not rotating then no thrust, so no steerage
  Rudder p.41
    Boats with a fixed propeller use a rudder to direct the flow of water
    Water flowing over the rudder creates lift (sideways force) and turns the boat
    No water flowing over the rudder = no steerage
  Pivot Point p.44
    In forward, a boats pivot point is located 25% to 40% aft from the bow
    Always steer the pivot point along the path you want to steer!
    Where is the pivot point on a boat in reverse?

## Slide 13: Maneuvering Concepts
Planing hulls behave like displacement hulls at low speed
At a certain speed, the hull goes through a transition stage called semi-displacement as it climbs the face of its bow wave p.47
Once the boat moves over the top of its bow wave, it levels off and begins to plane
Q: Where is the most optimum fuel consumption for a planing hull?
SPR p.47

## Slide 14: Safety Equipment: Lifejackets
    Type I – Offshore Life jacket
      22 lbs of buoyancy for adults / 11 lbs for children
      Will turn unconscious person face-up
    Type II – Near-Shore Life Vest
      Min. of 15.5 lbs for adults / 11 lbs for children
      Will turn some unconscious people face-up
    Type III – Flotation Aid
      Buoyancy the same as Type II
      Will not turn unconscious person face-up
      Most common
    Type IV – Throwable Device
    Type V – Special use Devices
      Inflatable vests, etc.
      No inherent buoyancy
      Must be worn!
SPR p.83

## Slide 15: Safety Equipment: Lifejackets

## Slide 16: Safety Equipment: Lifejackets
Lifejackets
  Proper use of PFDs is integral!
    Should fit snugly but still allow movement
    If you can pull it up around your head on land, the same thing will happen in the water
    Any PFD with a tear or hole in it is no longer Coast Guard approved

## Slide 17: Safety Equipment
Federal Requirements for boats under 26ft
  One life jacket for each person on board. Must be readily available.
    Children under 13 MUST wear a lifejacket while underway (on any size vessel) unless below decks or in an enclosed cabin
  Over 16ft – one Type IV throwable device
  Sound producing device p.85
    Air horn, whistle, manual horn, etc.
  Fire extinguisher p.85
    Under 26ft – one B-I
      A – combustible material (wood)
      B – flammable liquids (gas)
      C – electrical (wiring)
      D – combustible metals (magnesium)
  Under 16ft - Visual distress signals if used at night p.84
  16ft up – MUST carry approved day/night visual distress signals
SPR p.85

## Slide 18: Safety Equipment
Recommended Requirements
  Anchor + rode
  VHF Radio
  Knife
  First Aid Kit
  Spare parts / tool kit
  Oars
  Hand bilge pump
  Tow line / spare line

## Slide 19: Registration Information
Hull Identification Number
Registration numbers and form
  Boat must be registered in its state of principal use or federally documented
  ‘IL’ numbers must be displayed on each side of the bow in letters at least 3” high
  Registration must be aboard vessel at all times
Max capacity plate
  Displays maximum weight and # of passengers (# of passengers takes precedence)
  Displays maximum horsepower engine (on outboard)
  Displays maximum weight capacity of all passengers, engine and gear
  Capacity equation: L x B / 15
SPR p.82

## Slide 20: State Specific Information
INSTRUCTORS: Use this section to include specific information for the state in which you will be teaching Safe Powerboat Handling.
Examples: Marine Heads, Pollution Laws, Age of Operator, etc.

## Slide 21: BREAK