## Slide 1: Safe Powerboat Handling
Classroom Session One
Powerpoint 2 of 2

## Slide 2: Engine Information
Outboards
  Engine mounted on transom of boat
  2hp – 350+ hp
  2-stroke or 4-stroke
    2-strokes fire once every revolution of the crankshaft
        Power / intake-exhaust; compression
    4-strokes fire once every 2 revolutions of the crankshaft
        Intake – compression – power - exhaust
    2-strokes use a gas/oil mixture
    4-strokes use straight gas (oil is in the crankcase)
    Traditional 2-strokes are becoming obsolete
      Bad for the environment
      Less fuel efficient
SPR p.13

## Slide 3: Engine Information
Outboards
  Variable shaft lengths
  Can be tilted all the way up or removed for storage
  Parts of an outboard engine p.14

## Slide 4: Engine Information
Inboards
  Engine mounted inside boat
  Gasoline or diesel
    Diesel is safer than gas – less risk for fire
    Gas inboards MUST have a backfire flame arrestor
  3 types of drive options:
    Fixed propeller drives
      Prop shaft passes through bottom of boat
      Steered by a rudder
    Stern drive (I/O)
      Engine mounted inside and the power train goes through transom to the stern drive
      Stern drive has tilt and trim similar to an outboard
    Jet drive
      Impeller accelerates water through a nozzle to produce propulsive thrust
SPR p.20

## Slide 5: Engine Information
SPR p.20

## Slide 6: Engine Information
Proper fueling procedures
Common fueling mistakes
  Forget to vent the jerry can
  Nozzle not tightly attached to jerry can
  Overfilling
  Pouring one tank straight into another without a funnel or nozzle
  Pouring fuel into a deck fill that is NOT for fuel
SPR p.18, 25

## Slide 7: Engine Information
Proper start-up procedures for gas engines
  Inspect all hoses and wires
  Check fuel, oil and transmission fluid levels
  Run blower for 4 min (inboards)
  Lower engine into water (outboards and I/Os)
  Open vent, pump fuel primer bulb until firm
  Ensure that gear shift is in neutral
  Attach stop switch (kill switch)
  Pull cord / turn key to start
    Use choke and adjust idle as needed until running smoothly
  Once running, MAKE SURE THERE IS A STREAM OF WATER FLOWING FROM THE INSPECTION OUTLET
  Check gauges
SPR p.16, 21

## Slide 8: Engine Information
Gauge Guidelines
  Hour Meter
  Volt Meter
    12+ volts
  Oil Pressure
    MINIMUM of 20 PSI
  RPM –
    MAX Idle RPM of 800
  Temperature
    140-160 is normal; 180+ is overheating

## Slide 9: Engine Information
Troubleshooting
  Fuel – Spark – Compression!
  Nothing happens when you turn the key
    Spark – is the battery dead? Are you in neutral?
  Engine turns over but won’t catch
    Fuel – is the engine getting gas? Is there water in the gas? Is the fuel line attached backwards?
    STOP SWITCH!
  Engine runs fine at idle but kills when at higher RPM
    Spark – bad spark plug? Loose spark plug lead?

## Slide 10: Pre-Boarding Preparation
Check weather conditions
  Not just for today but for yesterday and tomorrow!
  Internet
    Weather.com
    Sailflow.com
    Intellicast.com
    NOAA.gov
  VHF
    WX channels – broadcast continual marine forecasts
SPR p.29

## Slide 11: Pre-Boarding Preparation
Check tides and currents
  Occasional current in mouths of harbors depending on wave/swell direction
      To check current, use a current stick or observe motion of water around a fixed object

## Slide 12: Pre-Boarding Preparation
File a Float Plan!
SPR p. 31

## Slide 13: Pre-Boarding Preparation
Complete Vessel Checklist
Example Checklist: Chicago Yacht Club

## Slide 14: BREAK

## Slide 15: Boat Operation
Proper boat storage – At the dock
  Engine raised and flushed (well….maybe)
  Steering wheel turned so steering arm is enclosed
  Lines checked and flemished
  Fenders hung at proper height
  Battery switched off (if appropriate)
  Any gear that was used stowed appropriately
  Bilge checked
  Garbage emptied

## Slide 16: Boat Operation
Proper boat storage – Ashore
  Trailer guidelines
    Be diligent with checking all aspects of trailer and connection
    Don’t settle – if boat isn’t seated properly, redo it
    Always remember to raise your engine before driving up the ramp!
    Check your tie downs multiple times.
SPR p.143

## Slide 17: Knots
www.animatedknots.com
  Cleat hitch
  Bowline
  Round turn w/2 half hitches
  Sheet bend
  Coiling and heaving
SPR p.35

## Slide 18: REVIEW QUESTIONS